Guitar Hero Hose Replacement Procedure p/n AS-2026

Parts list
1 - AS-2026 Hose
1 - 3-102 Washer
1 - 31-TP250-03-001 Screw
1 - Guitar Hanger
1 - 600-00112-01 Guitar Strap

Tools required to Install
#10 Security Torx Bit/Wrench
#20 Security Torx Bit/Wrench
#27 Security Torx Bit/Wrench
Drill
5/16” drill bit
Phillips Head Screw Driver
3/8” nut driver or ratchet and 3/8” socket

Using a #10 security torx wrench remove the 10 screws holding the faceplate to the guitar body. (As Illustrated below)

To remove the old hose you will need to remove the 2 #20 torx screws at the base of the guitar. As shown below.

Next using your Phillips Head screw driver remove the 4 screws securing the Strum assembly. Remove the 6 pin connector and lift the assembly out of the guitar.

Next using your #10 torx wrench you will need to remove the 6 screws securing the fret plate cover to the guitar body.

After removing the fret plate cover you will need to remove the 5 rubber keys.

Next turn the guitar over and using a #20 torx wrench remove the 4 screws (indicated by circles below) then using a #27 torx wrench remove screw securing the guitar strap hanger to the guitar body.(indicated by the arrow)
You can now slide the metal spline assembly down towards the base of the guitar. The hose cable connection is now accessible remove from connector as illustrated below.

You can now remove your old hose and the metal spline from the guitar.

As illustrated below by the arrows mark the center of your hole to be drilled 1 1/16” from the base of the formed indentation and 1” up from the side of the indentation. Using your 5/16” drill bit drill the new guitar strap hanger hole.

1 1/16”

1”

You can now insert your new hose cable into the base of the guitar.
After reconnecting your 10 pin connector on your new cable to the fret PCB you will need to secure the ground wire to the bolt on the metal frame as shown below.

Now slide the metal spline assembly back up into the neck positioning it over the mounting holes on the rear of the guitar body and re-install the screws you previously removed. You will now also attach the strap hangers to the backside of the guitar body as shown below.

You can now reinstall the fret cover plate and the strum assembly faceplate using the screws removed previously.

If you have any questions please call 800-753-2513 for technical assistance.